## Slide 1: Delta Intelligent Smart Screw System Version 25.07
DET-AMBU

## Slide 2
Smart screw system Architecture

## Slide 4: Software of Smart screw System
Product Navigate Show points and sequence control follow OI
Sequence Control Parameter tightening control and recording tightening results.
Line Chart show torque/time, torque rate/ time
Smart Screw & ARM display show smart screw connection status and tightening results and show coordinate ARM position
PQM & MES & DIASSA Upload PQM, MES, DIASSA
Realtime & Status bar Show serial number, current step and status

## Slide 6
Smart screw structure

## Slide 7
Type | A | A+ | C | C+ | N | D | D+ | NS
Module |  |  |  |  |  |  |  | 
Non-touch screw | YES | YES | YES | YES | YES | YES | YES | YES
Solution function | Direct shoot screw | Direct shoot screw &tool change | Direct shoot screw (magnet) | Direct shoot screw (Magnet Tool change) | Pick screw (magnet) | Pick screw (Vacuum) | Pick screw (Vacuum Tool change) | Pick screw (magnet Top & Front screw)
Delta smart screw system (DIASSA) | YES | YES | YES | YES | YES | YES | YES | YES
Arm sequent control | YES | YES | YES | YES | YES | YES | YES | YES
Multi screw type | 1 | 1-3 | 1 | 1-3 | 1-3 | 1 | 1-3 | 1-3
Function drop detection | YES | YES | NO | NO | NO | YES | YES | NO
Smart screw module

## Slide 8
Application specification

## Slide 9
Delta Swing Torque arm dimension
Swing 450
Swing 650
Swing 950

## Slide 10
Delta Slide Torque arm dimension
Model | Slide 450 mm | Slide 650 mm | Slide 1000 mm | Slide 1250 mm
Tool Ø (mm) | 28-52 | 28-52 | 28-52 | 28-52
B. Stroke(mm) | 450 | 650 | 1000 | 1250
C. Max load(Kg) | 3.0 | 3.0 | 3.0 | 3.0

## Slide 11
Workspace simulation
Fix on front right of operator
Fix on front inside of operator

## Slide 12
Delta Screwdriver

## Slide 13
Blow Screw feeder
MRO PN | Model | Description
A00100301914 | AM-H0503002-0000 | Screw feeder tube M3-4
A00100301915 | AM-H0503002-1000 | Screw feeder tube M5-6
A00100302336 | AM-H0503002-2000 | Screw feeder Long lift M3-4
A00100302332 | AM-H0503002-2001 | Screw feeder Long lift M5-6
A00100302331 | AM-H0503002-5000 | Nut feeder Tube shoot

## Slide 14
Smart screw feeder
MRO PN | Model | Description
A00100302337 | AM-H0503002-3000 | ASSY SCREW FEEDER PICK&PULL OUT M2-M6
A00100302333 | AM-H0503002-3004 | ASSY SCREW FEEDER PICK&PULL OUT M2-M8
A00100302338 | AM-H0503002-4000 | ASSY SCREW FEEDER SIDE ROTATION M2-M6
A00100302334 | AM-H0503002-4002 | ASSY SCREW FEEDER SIDE ROTATION M2-M6